## Slide 1: Designing a Battery Management System From a Real-Time System Perspective
Jinkyu Lee
Dept. of Computer Science and Engineering,
Sungkyunkwan University (SKKU)
2022.9.21-22 Samsung SDI

## Slide 2: Overall Schedule
1차시 (신동화 교수님)
  9/19(월) 13~16시
  실시간 시스템의 개념
2차시
  9/21(수) 9~12시
  실시간 태스크 스케줄링 기법
3차시
  9/22(목) 13~16시
  실시간 태스크 스케줄링 가능성 (Schedulability) 분석 기법
추후
  배터리 관리 시스템의 태스크 구성과 스펙에 따른 실시간 시스템 성능 요구 분석 (현재 BMS 스펙 등을 검토 및 토의)
Designing a Battery Management System From a Real-Time System Perspective

## Slide 3: Schedule for each day
(9/21)
09:00 – 10:15
  Lecture
10:15 – 10:30
  Break
10:30 – 11:45
  Lecture
11:45 –
  Q&A
(9/22)
13:00 – 14:15
  Lecture
14:15 – 14:30
  Break
14:30 – 15:45
  Lecture
15:45 –
  Q&A

## Slide 4: REVIEW OF THE PREVIOUS LECTURE

## Slide 5: Real-Time Scheduling
Real-time task model
Concept of scheduling algorithm and schedulability analysis
Priority-driven scheduling algorithm
  Fixed-priority scheduling (e.g., Rate Monotonic)
  EDF
Schedulability analysis
  Utilization-based analysis
  Response time analysis

## Slide 6: Real-Time Scheduling
Uniprocessor: at each time slot, only one job can be executed.
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
τ1
τ2
τ3
T1=4, D1=4, C1=1
Deadline miss
τ1 > τ2 > τ3, non-preemptive
τ1 > τ2 > τ3, preemptive

## Slide 7: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo
Why this is possible?
Scheduling algorithm + Schedulability analysis

## Slide 8: Real-Time Scheduling
Two main components for real-time scheduling
  Scheduling algorithm
    Determine when each job executes (which job to be executed)
  Schedulability analysis
    Guarantee no deadline miss of a given task set under the target scheduling algorithm
Scheduling
Algorithm
Can we guarantee no deadline miss in the future?
Schedulability Analysis

## Slide 9: Real-Time Scheduling
Why do we need schedulability analysis? Isn’t it possible to guarantee schedulability simply by simulating a target set of tasks?
  Is it possible to simulate all different combinations of offsets?
  Can each simulation guarantee the schedulability even with actual execution times less than their corresponding WCETs?
  Is it feasible to simulate a target set of tasks if their LCM is very large?
Scheduling
Algorithm
Schedulability Analysis
Can we guarantee no deadline miss in the future?

## Slide 10: Real-Time Scheduling
Which scheduling algorithm with which condition (i.e., schedulability analysis) guarantees that there is no single job deadline miss forever?
  With any offset,
  With any actual execution time,
  With any arbitrary long period,
Scheduling
Algorithm
Schedulability Analysis
Example
Can we guarantee no deadline miss in the future?

## Slide 11: Classification of Priority-Driven Scheduling
Can we guarantee no deadline miss of all jobs of a given task set under each scheduling algorithm?
  TFP: RM
  JFP: EDF
  JDP: LLF
What is the maximum utilization?
  U = ∑ Ci/Ti ≤ 1.0
    Example: 1/4 + 2/5 + 2/7
Can each scheduling algorithm achieve the maximum utilization?

## Slide 12: RM: Overview
  Critical instant under RM
Utilization-based analysis
  U ≤ n(21/n – 1.0)
    n → ∞, n(21/n – 1.0) → 0.69
  Only sufficient
Response-time analysis
  Exact
Some applications
  Schedulability with transient overhead, interrupts and blocking
Without loss of generality
T1 ≤ T2 ≤… ≤ Tn

## Slide 13: RM: Critical Instant
Critical instant of τi
  A job of τi arriving at that instant has the largest response time
  Which τ2 has the maximum response time?
In-phase instant is critical under RM
  All higher priority tasks are released at the same instant of Ji,c (assume all jobs are completed before the next job is released)
Task1 Task2
Task1, Task2
Task2 Task1
Why?

## Slide 14: RM: Utilization-Based Analysis
Example
  Total utilization is
.200 + .267 + .286 = .753 < U(3)=3(21/3 – 1.0)=.779
  The periodic tasks in the example are schedulable according to the UB test.
 | Ci | Ti | Ui
Task1 | 20 | 100 | 0.200
Task2 | 40 | 150 | 0.267
Task3 | 100 | 350 | 0.286
  U ≤ n(21/n – 1.0)

## Slide 15: SYNCHORNIZATION

## Slide 16: Priority inversion
Priority-based preemptive scheduling
  Priority represents importance or urgency.
However, a higher-priority task can be blocked by a lower-priority task, i.e., priority inversion
  Execution with critical section
    Mutex for shared resource access
    Non-preemptive sub-systems access, e.g., system bus, secondary storage, network, etc.

## Slide 17: No priority inversion
τH
τM
τL
τH
τM
τL
Released at t=2
Released at t=4
Released at t=0
…
…

## Slide 18: Priority inversion
τH
τM
τL
τH
τM
τL
Released at t=2
Released at t=4
Released at t=0
normal execution
execution with critical section
lock(R)
request_lock(R)
unlock(R)
lock(R)
unlock(R)
…
…

## Slide 19: Priority inversion
It is not harmful, most of time.
  Some additional delays for higher-priority tasks
However, it can be very critical at some point
  Example: Mars Pathfinder

## Slide 20: Mars Pathfinder
Landed on the Mars on July 4th, 1997.
  Surface operations
  Daily images of Mars
  Daily weather reports from the surface of Mars
Out-of-control, due to a software problem
July 4th
July 12th
July 19th
Landed
Successful
operations
Communication errors
Problem solved
What happened?
  http://nssdc.gsfc.nasa.gov/planetary/mesur.html

## Slide 21: Mars Pathfinder
  τH: information bus task (short, frequent)
    Should have quick responses
  τM: communication task
  τL: meteorological task
…
Total system reset!
τH
τM
τL
lock(R)
request_lock(R)
unlock(R)
lock(R)
unlock(R)

## Slide 22: Synchronization protocols
Priority inheritance protocol (PIP)
Priority ceiling protocol (PCP)
  Lui Sha, Raj Rajkumar, John Lehoczky, “Priority Inheritance Protocols: An Approach to Real-Time Synchronization,” IEEE Transactions on Computers, vol. 39, no. 9, page 1175-1185, 1990.

## Slide 23: Priority inheritance protocol (PIP)
A higher-priority task inherits its priority to a lower-priority task
  When the higher-priority task waits for the resource locked by the lower-priority task
τL inherits τH’s priority
τH
τM
τL
lock(R)
request_lock(R)
unlock(R), the inheritance ends
lock(R)
unlock(R)
…

## Slide 24: Priority inheritance protocol (PIP)
τL inherits τH’s priority
τH
τM
τL
lock(R)
request_lock(R)
unlock(R), the inheritance ends
lock(R)
unlock(R)
τH
τM
τL
lock(R)
request_lock(R)
unlock(R)
lock(R)
unlock(R)
…
…

## Slide 25: Priority inheritance protocol (PIP): Deadlock
What if there are two types of critical sections?
normal execution
R1
execution with critical section
R2
τH
τL
Released at t=2
Released at t=0
τH
τL
lock(R2)
request_lock(R2)
lock(R1)
request_lock(R1)
Deadlock!

## Slide 26: Priority ceiling protocol (PCP)
PIP + the following mechanism
  A task can lock a resource only if its priority is strictly higher than all the ceilings of the resources currently locked by other tasks.
request_lock(R1)
Ceiling(R2)= τH
No lock(R1)
τH
τL
lock(R2)
lock(R1)
unlock(R1)
unlock(R2)
lock(R1)
lock(R2)
unlock(R1)
unlock(R2)
Ceiling(R1)= τH
Ceiling(R2)= τH

## Slide 27: Priority ceiling protocol (PCP)
request_lock(R1)
Ceiling(R1)= τH
No lock(R1)
τH
τL
lock(R2)
lock(R1)
unlock(R1)
unlock(R2)
lock(R1)
lock(R2)
unlock(R1)
unlock(R2)
τH
τL
lock(R2)
request_lock(R2)
lock(R1)
request_lock(R1)
Deadlock!

## Slide 28: Priority ceiling protocol (PCP)
Proved that
  PCP prevents chained blocking and deadlocks; and
  A task can be blocked for at most the duration of one critical section.

## Slide 29: Synchronization protocols: Where are we?
Synchronization Protocols
Schedulability Analyses
Uniprocessor
Identical multicore
Heterogeneousmulticore
Periodic resources
Fully mature
Fully mature
Some studies
Some studies
Few studies

## Slide 30: CASE STUDY: BMS SYSTEM

## Slide 31: Case Study
BMS system
  Task model
    Periodic tasks except for initialization tasks (start-up & shutdown)
    Initialization tasks perform only for start-up and shutdown
  The source of WCET
    Measuring the max execution time
  Task dependency
    No control flow dependency
    No shared resource

## Slide 32: Case Study
BMS system
  Prioritization
Rate Monotonic
Priority-driven,
TFP
Mixture of
Non-preemptive & Preemptive

## Slide 33: Case Study

## Slide 35: Case Study
(T, C) task model
  Preemptive, no preemption cost
  No offset
  Fixed-priority scheduling (e.g., Rate Monotonic scheduling)
  Focus on a single processor (i.e., no interference between cores)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
Runnable | Runnable Priority | Offset | max execution time [ns] | Period[ms]
SbcM_MainFunction | 0 | 0 | 515520 | 100
SbcM_MainFunction_10ms | 2 | 0 | 28000 | 10
R_DIS | 10 | 0 | 2080 | 20
R_MCI | 12 | 85 | 633280 | 50
ms
regulated
Priority: τ1 > τ2 > τ3 > τ4
=> 0

## Slide 36: Case Study
Applying response-time analysis
  R1
    R1 = 6 (≤ 100, schedulable)
  R2
    a=6+4=10 => 10
    R2 =10 (≤ 10, schedulable)
  R3
    a=6+4+1=11 => 15
    a=15 => 15
    R3 =15 (≤ 20, schedulable)
  R4
    a=6+4+1+20=31 => 44
    a=44 => 49
    a=49 => 49
    R4 =49 (≤ 50, schedulable)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20

## Slide 37: Case Study
(T, C) task model
  Preemptive, no preemption cost
  No offset Non-trivial offset
  Fixed-priority scheduling (e.g., Rate Monotonic scheduling)
  Focus on a single processor (i.e., no interference between cores)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
Runnable | Runnable Priority | Offset | max execution time [ns] | Period[ms]
SbcM_MainFunction | 0 | 0 | 515520 | 100
SbcM_MainFunction_10ms | 2 | 0 | 28000 | 10
R_DIS | 10 | 0 | 2080 | 20
R_MCI | 12 | 85 | 633280 | 50
ms
regulated
Priority: τ1 > τ2 > τ3 > τ4

## Slide 38: Case Study
Applying response-time analysis AS IT IS
  Why?
    Critical instances
(50,20)
τ4
(10,4)
τ2
(10,4)
τ2
(50,20)
τ4

## Slide 39: Case Study
(T, C) task model
  Preemptive, no preemption cost Non-preemptive
  No offset Non-trivial offset
  Fixed-priority scheduling (e.g., Rate Monotonic scheduling)
  Focus on a single processor (i.e., no interference between cores)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
Runnable | Runnable Priority | Offset | max execution time [ns] | Period[ms]
SbcM_MainFunction | 0 | 0 | 515520 | 100
SbcM_MainFunction_10ms | 2 | 0 | 28000 | 10
R_DIS | 10 | 0 | 2080 | 20
R_MCI | 12 | 85 | 633280 | 50
ms
regulated
Priority: τ1 > τ2 > τ3 > τ4
NP
NP
NP
NP

## Slide 40: Case Study
Can we apply response-time analysis as it is?
  NO!
Can a lower-priority block a higher-priority task?
  When?
What are the differences?
  In terms of interfering
  In terms of being interfered
What is the critical instance?
  For the lowest-priority task
  For the highest-priority task
  For other tasks?
(10,4)
τ2
(50,20)
τ4

## Slide 41: Case Study
Modifying the response-time analysis
  A job of the lower-priority task τi can block a job of the higher-priority task τk only when τi starts its execution before is τk released.
  A job of the higher-priority task can be blocked by only one job of any lower-priority tasks.
A set of higher-priority tasks
+ max
A set of lower-priority tasks
Can we apply critical instant for the preemptive model to that for the non-preemptive model?

## Slide 42: Case Study
Applying response-time analysis
  R1
    R1 = 6+19 (≤ 100, schedulable)
  R2
    a=6+4+19=29
    R2 ≥ 29 (>10, unschedulable)
  R3
    a=6+4+1+19 =30
    R3 ≥ 30 (>20, unschedulable)
  R4
    a=6+4+1+20=31 => 44
    a=44 => 49
    a=49 => 49
    R4 =49 (≤ 50, schedulable)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20

## Slide 43: Case Study
Check whether a task starts its execution at t,
  Instead of whether a task finishes its execution at t.
What is the difference?
A set of higher-priority tasks
+ max
A set of lower-priority tasks

## Slide 44: Case Study
  R3
    a=6+3+5=14 => 17
    a=17 => 17
    R3 =17 (≤ 20, schedulable)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 3
τ3 | 20 | 5
  F3
    a=6+3+1=10 => 10
    F3 =10
     R3 = F3 +(C3-1) = 10+4=14
    (≤ 20, schedulable)

## Slide 45: Case Study
(T, C) task model
  A mixture of preemptive and non-preemptive
  No offset Non-trivial offset
  Fixed-priority scheduling (e.g., Rate Monotonic scheduling)
  Focus on a single processor (i.e., no interference between cores)
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
Runnable | Runnable Priority | Offset | max execution time [ns] | Period[ms]
SbcM_MainFunction | 0 | 0 | 515520 | 100
SbcM_MainFunction_10ms | 2 | 0 | 28000 | 10
R_DIS | 10 | 0 | 2080 | 20
R_MCI | 12 | 85 | 633280 | 50
ms
regulated
Priority: τ1 > τ2 > τ3 > τ4
P
NP
NP
P

## Slide 46: Case Study
Can we apply response-time analysis as it is?
  NO!
What are the differences?
  4 cases (interfered, interfering)
    P: preemptive, NP: non-preemptive
    (P ← P), (P ← NP), (NP ← P), (NP ← NP)
What is the critical instance?
  For the lowest-priority task
  For the highest-priority task
  For other tasks?

## Slide 47: Case Study
(P ← P)
(P ← NP)
(NP ← P)
(NP ← NP)
→ A set of non-preemptive lower-priority tasks
→ A set of non-preemptive lower-priority tasks
Can we apply critical instant for the preemptive model to that for the mixture model?

## Slide 48: Case Study
(T, C) task model + initialization task
  A mixture of preemptive and non-preemptive
  No offset Non-trivial offset
  Fixed-priority scheduling (e.g., Rate Monotonic scheduling)
  Focus on a single processor (i.e., no interference between cores)
Runnable | Runnable Priority | Offset | max execution time [ns] | Period[ms]
SbcM_MainFunction | 0 | 0 | 515520 | 100
SbcM_MainFunction_10ms | 2 | 0 | 28000 | 10
R_DIS | 10 | 0 | 2080 | 20
R_MCI | 12 | 85 | 633280 | 50
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
ms
regulated
P
NP
NP
P

## Slide 49: Case Study
Add the execution time of the initialization task only once.
What about the shut-down task?
 | Period | WCET
τ1 | 100 | 6
τ2 | 10 | 4
τ3 | 20 | 1
τ4 | 50 | 20
ms
regulated
P
NP
NP
P

## Slide 50: Case Study
More general, complex case
  Interference between cores
  Dependency between tasks
    Example: shared resources, precedency relationship
  Limited preemption
  Multiple computing cores
    Global scheduling
    Partitioned scheduling
  More general, complex task model
    E.g., DAG-structured tasks
Each issue is a research topic, yielding a number of academic papers.

## Slide 51: Case Study: Conclusion
As the task model, constraints and platforms get more complex, it also becomes more complex to derive the schedulability analysis.
  However, it is usually possible to derive schedulability analysis.
    At least in the settings we discussed so far.
  Also, the result of the schedulability analysis is less complex than the derivation of the schedulability analysis.

## Slide 52: THE END
Thank you for attending this class!

## Slide 54: MULTIPROCESSOR SCHEDULING

## Slide 55: What have we done so far for task scheduling?
Scheduling a set of tasks with various constraints on a single processor.
What should we do if schedulability condition for the given task set cannot be met?
Question: which tasks should be assigned to which processors and why?
Ideally, combined task assignment and scheduling is desirable, but this is very hard.
Common approach: assign tasks and then schedule them on each processor.

## Slide 56: Summary: periodic tasks
T1
D1=4
T1=5
T1
τ1
A job of Task 1
Source: http://aar.faculty.asu.edu/research/mosart/mosart.html
sensor
actuator
control law
computation
A/D
reference input
D/A
D1
D1
C1=2
Source: “Task Scheduling for Control Oriented Requirements for Cyber-Physical Systems,” RTSS 2008.

## Slide 57: Summary: uniprocessor scheduling
Practice
Theory
Soft deadline
Dependent task model, e.g., resource sharing
Hierarchical model (virtualization)
  A single processor
  Hard deadline
  Independent periodic tasks
  Di = Ti
  Preemptable without any limit and overhead for context switch
Preemption cost
analysis
VxWorks, Xen, RT Linux
Di ≤ Ti
Non-preemptive scheduling

## Slide 58: Summary: uniprocessor scheduling
Task-level fixed-priority (TFP)
  RM (Rate-monotonic): optimal TFP
    Utilization-based analysis: U ≤ n(21/n – 1.0) (only sufficient)
    Response-time analysis (exact)
Job-level fixed-priority (JFP)
  EDF (Earliest Deadline First): optimal
    U ≤ 1.0 (exact)
Job-level dynamic-priority (JDP)
  Least Laxity First (LLF): optimal
    U ≤ 1.0 (exact)

## Slide 59: Multiprocessor scheduling
Assumptions
  m identical processors (homogeneous)
  Hard deadlines
  Independent periodic tasks
  Relative deadline = period (Di = Ti)
  Preemptable without any limit
  No overhead for context switch

## Slide 60: Multiprocessor scheduling
How are tasks assigned to processors?
Static assignment (static binding)
  The processor(s) used for executing a task are determined before system is put in mission (“off-line”)
  Approach: partitioned scheduling
Dynamic assignment
  The processor(s) used for executing a task/job are determined during system operation ( “on-line”)
  Approach: global scheduling

## Slide 61: Multiprocessor scheduling
Are tasks allowed to migrate?
Partitioned scheduling – No migration
  Each instance of a task must execute on the same processor
  Equivalent to multiple uniprocessor systems
Global scheduling
  Full migration
  A task is allowed to execute on any processor
  Migration can occur even during execution of an instance of a task (for example, after being preempted)
Semi-partitioned scheduling
  No migration for some tasks, and full migration for other tasks

## Slide 62: Partitioned vs. global static-priority scheduling
Incomparable [Leung and Whitehead’82] for TFP
  (A) There are task systems that are feasible on m processors under partitioned approach but for which no priority assignment exists which would cause all jobs of tasks to meet their deadlines under global scheduling on m processors; and
  (B) There are task systems that are feasible on m processors under global approach, but which cannot be partitioned into m distinct subsets such that each partition is uniprocessor static-priority feasible.
  Leung and Whitehead, “On the complexity of fixed priority scheduling of periodic, real-time tasks,” Performance Evaluation, 2(4), Dec. 1982

## Slide 63: Partitioned vs. global static-priority scheduling
Incomparable [Leung and Whitehead’82] for TFP
  (A) There are task systems that are feasible on m processors under partitioned approach but for which no priority assignment exists which would cause all jobs of tasks to meet their deadlines under global scheduling on m processors.
    Example: m=2, Task 1(2,1), Task 2(4,2), Task 3(3,2), Task 4(6,2)
      Easily schedulable by partitioned scheduling
      But, there exists no task-level assignment that makes the task set schedulable

## Slide 64: Partitioned vs. global static-priority scheduling
Incomparable [Leung and Whitehead’82] for TFP
  (B) There are task systems that are feasible on m processors under global approach, but which cannot be partitioned into m distinct subsets such that each partition is uniprocessor static-priority feasible.
    Example: m=2, Task 1(3,2), Task 2(6,4), Task 3(12,5)
      Never be schedulable by any partitioned scheduling
      But, schedulable by TFP with priority (Task 1 > 2 > 3)

## Slide 65: Multiprocessor scheduling
A fundamental limit [ABJ01]
  For any scheduling (partitioned or global) with TFP and JFP, the utilization bound cannot be higher than 50% (=m/2)
  Example
    m processors
    m+1 tasks: Ti=2L-1, Ci=L, released at 0
    Utilization: L/(2L-1)*(m+1) → ½*m, if L → ∞
    What happens with partitioned scheduling in [0, 2L-1]?
    What happens with global scheduling in [0, 2L-1]?
[ABJ01] Bjorn Andersson, Sanjoy Baruah, Jan Jonsson, “Static-priority scheduling on multiprocessor”, RTSS 2001, pp. 193-202.
BTW, what is the utilization bound?
Notes: U(tau) <=m^2/(3m-2) on m identical processors

## Slide 66: Multiprocessor scheduling
  What happens with partitioned scheduling in [0, 2L-1]?
    With any TFP, JFP and JDP
2L-1
…
…
P1
P2
P3
Pm
τ1
τ2
τ3
τm
τm+1
L
Not feasible!

## Slide 67: Multiprocessor scheduling
  What happens with global scheduling in [0, 2L-1]?
    With any TFP and JFP
2L-1
…
…
P1
P2
P3
Pm
τ1
τ2
τ3
τm
τm+1
L
Not feasible!

## Slide 68: Multiprocessor scheduling
  What happens with global scheduling in [0, 2L-1]?
    With JDP (e.g., LLF)
2L-1
…
…
P1
P2
P3
Pm
τ1
τ2
τ3
τm
τm+1
L
Feasible!

## Slide 69: Multiprocessor scheduling
A fundamental limit – more accurate statement
  For any partitioned scheduling (with TFP, JFP and JDP), the utilization bound cannot be higher than 50% (=m/2)
  For any global scheduling with TFP and JFP, the utilization bound cannot be higher than 50% (=(m+1)/2)
    What about global scheduling with JDP?
  Dhall’s effect: It is possible to find a task set that is unschedulable although it consumes any arbitrarily small fraction of the multiprocessor platform
Notes: U(tau) <=m^2/(3m-2) on m identical processors
Dhall’s effect:
U->1 no matter how many processors are used
for T1=T2=…=Tm=(2e,1), T_(m+1)=(1,1+e) on m identical unit-speed processors where Ti=(Ci, Pi)
I.e., it is possible to find a task set that is unschedulable although it consumes only an arbitrarily small fraction of the multiprocessor platform.

## Slide 70: Partitioned scheduling
Each processor has its own queue for ready tasks
Tasks are organized in groups, and each task group is assigned to a specific processor
  For example, using a bin-packing algorithm
When selected for execution, a task can only be dispatched to its assigned processor, i.e., static-binding

## Slide 71: Partitioned scheduling
Advantages:
Mature scheduling framework
  Most uniprocessor scheduling theory is also applicable
  Uniprocessor resource-management protocols can be used
Supported by automotive industry
  AUTOSAR adopts partitioned scheduling
Disadvantages:
Cannot exploit all unused execution time
  Surplus capacity cannot be shared among processors
  Will suffer from overly-pessimistic WCET derivation

## Slide 72: Partitioned scheduling
Bin-packing algorithms:
Basic idea:
  Packs the objects of varying sizes in boxes (“bins”) with the objective of minimizing # of boxes to use.
Application to multiprocessor systems:
  Bins are represented by processors and objects by tasks.
  Whether a processor is “full” or not is determined by a utilization-based feasibility test.
Assumptions:
  Independent, periodic tasks
  Preemptive, uniprocessor scheduling (e,g., RM)

## Slide 73: Global scheduling
All ready tasks/jobs are kept in a common (global) queue that is shared among the processors
Whenever a processor becomes idle, a task/job from the global queue is selected for execution on that processor.
After being preempted, a task/job may be dispatched to a processor other than the one that started executing it.

## Slide 74: Global scheduling
Advantages:
Supported by most multiprocessor operating systems
  Windows 7, Mac OS X, Linux, ...
Effective utilization of processing resources
  Unused processor time can easily be reclaimed, e.g., when a task does not execute its full WCET.
Disadvantages:
Weak theoretical framework:
“Few of the results obtained for a single processor generalize directly to the multiple processor case; bringing in additional processors adds a new dimension to the scheduling problem. The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors” [Liu69].
[Liu69] C.L.Liu, “Scheduling algorithms for multiprocessors in a hard real-time environment,” JPL Space Programs Summary, vol. 37-60, pp. 28-31, 1969.

## Slide 75: Reasons for weak theoretical results
  Dhall’s effect[DhLi78]
  With RM and EDF, some low-utilization task sets can be unschedulable regardless of how many processors are used. Thus, any utilization guarantee bound would become so low that it would be useless in practice.
  This is in contrast to the uniprocessor case where we have utilization guarantee bounds of 69.3% (RM) and 100% (EDF).
Hard-to-find critical instant
  A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.
  This is in stark contrast to the uniprocessor case!
[DhLi78] S.K. Dhall and C. L. Liu, “On a real-time scheduling problem,” Operations Research 26(1), 1978, pp.127-140.

## Slide 76: Reasons for weak theoretical results
Dhall’s effect
  Example (EDF or RM)
    m processors
    m+1 tasks: m tasks (1, 2*∆), 1 task (1+ ∆, 1)
…
P1
P2
P3
Pm
…
τ1
τ2
τ3
τm
τm+1
*10
1
∆
Deadline Miss at 1+ ∆
Utilization= m*2*∆/1 + 1*1/(1+ ∆)
if ∆→0, U→1 << m
∆
∆

## Slide 77: Reasons for weak theoretical results
Hard-to-find critical instant
  RM on uniprocessor
    Synchronous release is the critical instant
  RM on multiprocessor
    Synchronous release is NOT the critical instant
  Example
    2 processors, 4 tasks: (4,2), (4+∆,2), (4+2*∆,2) (4+3*∆,2)

## Slide 78: Reasons for weak theoretical results
Hard-to-find critical instant (RM)
    2 processors, 4 tasks: (4,2), (4+∆,2), (4+2*∆,2) (4+3*∆,2)
    Sync-release (released at t=0)
    Task 2 released at t=1, and others released at t=0
P1
P2
1
1
2
2
3
3
4
4
τ1
τ2
τ3
τ4
1
1
2
2
3
3
4
4
P1
P2
1
1
2
2
3
3
4
Deadline Miss at 4+3*∆
Response time of Task 4 = 4
Response time of Task 4 > 4

## Slide 79: Research trend: how to beat the weak theoretical results
Scheduling algorithm
  Design better algorithms than EDF and RM
  Make the algorithms ease the development of schedulability analyses
Schedulability analysis
  Develop schedulability analyses of EDF and RM, and then extend the developed techniques to more complex algorithms
  Consider the worst-case release pattern (since we don’t know the critical instant)
The critical instant
  Find some conditions for the critical instant, and incorporate the conditions to existing schedulability analyses

## Slide 80: Global scheduling: utilization-based analysis
TFP
  RM-US: U ≤ m2/(3m-1) ≈ 0.33*m, and more studies
JFP
  EDF-US: U ≤ m2/(2m-1) ≈ 0.5*m, and more studies
JDP
  Fluid scheduling: U ≤ m (optimal)
Notes: US

## Slide 81: Global scheduling: utilization-based analysis
RM-US[ABJ01]
  The algorithm gives the highest priority to tasks with utilization greater than m/(3m-2), and otherwise assigns priorities in RM order.
  Then, RM-US can schedule any task set with utilization less than m2/(3m-1) ≈ 0.33*m
  Example
    2 processors with Task 1(8,1), Task 2(10,6), Task 3(20,1)
      Priorities by RM: Task 1 > Task 2 > Task 3
      Priorities by RM-US: Task 2 > Task 1 > Task 3
      Schedulable by RM-US?
[ABJ01] Bjorn Andersson, Sanjoy Baruah, Jan Jonsson, “Static-priority scheduling on multiprocessor”, RTSS 2001, pp. 193-202.

## Slide 82: Global scheduling: utilization-based analysis
EDF-US[SrBa02]
  The algorithm gives the highest priority to tasks with utilization greater than m/(2m-1), and otherwise assigns priorities in EDF order.
  Then, EDF-US can schedule any task set with utilization less than m2/(2m-1) ≈ 0.5*m
  Example
    2 processors with Task 1(5,1), Task 2(5,1), Task 3(11,10)
      Any job of Task 3 always has the highest priority.
      Schedulable by EDF-US?
[SrBa02] A. Srinivansan and S.K. Baruah, “Deadline-based scheduling of periodic task systems on
Multiprocessors,” Information Processing Letters, 84:93–98, 2002.

## Slide 83: Global scheduling: optimal scheduling
Fluid scheduling
  In any interval of length L, jobs of Task x execute exactly L*Cx/Tx
  Example,
    2 processors with Task 1(3,2), Task 2(4,3), Task 3(12,7)
    U=2/3 + 3/4 + 7/12 = 2
12
9
8
7
Amount of execution
Time

## Slide 84: Global scheduling: optimal scheduling
Fluid scheduling
  Fluid scheduling cannot work in reality.
    Needs infinitesimal quantum length
  What if the quantum length is a clock tick, e.g., 1?
    In [0,1), the amount of execution for the two tasks is 1, while that of the unexecuted task is 0.
How to simulate fluid scheduling without any deadline miss?
12
7
Amount of execution
Time

## Slide 85: Global scheduling: optimal scheduling
Fluid scheduling
  Pfair[BCP96], ERfair[AnSr01], DP-fair[LFS10], RUN[RLM11], and more
    These algorithms incur many preemptions/migrations
      It is a very critical issue to reduce the number of preemptions/migrations
  Exact analysis
    U ≤ m (optimal)
[RLM11] P. Regnier, G. Lima, E. Massa, G. Levin, and S. A. Brandt, “Run: Optimal multiprocessor real-time scheduling via reduction to uniprocessor,” in RTSS, 2011.
[LFS10] G. Levin, S. Funk, C. Sadowski, I. Pye, and S. A. Brandt, “Dp-fair: A simple model for understanding optimal multiprocessor scheduling,” in ECRTS, 2010.
[BCP96] S. Baruah, N. K. Cohen, C. G. Plaxton, and D. A. Varvel, “Proportionate progress: a notion of fairness in resource allocation,” Algorithmica, vol. 15, no. 6, pp. 600–625, 1996.
[AnSr01] J.H.Anderson and A.Srinivasan, “Mixed Pfair/ERfair scheduling of asynchronous periodic tasks,” in ECRTS, 2001.

## Slide 86: Global scheduling: optimal scheduling
Pfair
  Idea: split a task into multiple tasks with execution time 1, and then schedule split tasks by EDF
    EDF can schedule a task set with U ≤ m if every task in the task set has execution time 1.
  Example
    2 processors with Task 1(8,4), Task 2 (11,8), Task 3 (3,2)
    How to split Task 2 and Task 3? (11/8,1) doesn’t make sense.
T1
T1’

## Slide 87: Global scheduling: optimal scheduling
Pfair
  Example
    Task 2 (11,8)
T1’
T1
Release: Floor(11/8*(i-1))
Deadline: Ceil(11/8*i)
i=1
Release: Floor (11/8*0)=0
Deadline: Ceil(11/8)=2
i=3
Release: Floor(11/8*2)=2
Deadline: Ceil(11/8*3)=5
Actual release time = max(virtual release time of i, finishing time of (i-1))

## Slide 88: Global scheduling: response time analysis
Response-time analysis framework[BeCi07]
  RM on a uniprocessor
    The critical instant: synchronous release
      The maximum amount of execution of Task j in an interval of length L
        Ceil(L/Tj)*Cj
[BeCi07] M. Bertogna, M. Cirinei, Response-time analysis for globally scheduled symmetric multiprocessor platforms, in: Proceedings of IEEE Real-Time Systems Symposium, 2007, pp. 149-160.
A set of higher-priority tasks
L
Cj
Cj
an+1 = Ci+∑Ceil(an/Tj)*Cj
e.g., (3,1), (5,2), (20,3)

## Slide 89: Global scheduling: response time analysis
Response-time analysis framework[BeCi07]
      Ceil(L/ Tj)*Cj
  RM on a multiprocessor
    We don’t know the critical instant
    The maximum amount of execution of Task j in an interval of length 1
      Ceil((L+ Tj -Cj) / Tj)*Cj
Cj
Cj
L
Cj
Cj
L
Cj
an+1 = Ci+∑Ceil(an/ Tj)*Cj
an+1 = Ci+Floor(∑Ceil((an+Tj-Cj)/Tj)*Cj/m)

## Slide 90: Global scheduling: response time analysis
Response-time analysis framework[BeCi07]
  RM on a multiprocessor
      Ceil((L+Tj-Cj) / Tj)*Cj
  Why is this working? Why Floor?
Cj
Cj
L
Cj
an+1 = Ci+Floor(∑Ceil((an+ Tj -Cj)/ Tj)*Cj/m)

## Slide 91: Global scheduling: response time analysis
Response-time analysis framework[BeCi07]
  There are some more techniques that can decrease the upper-bound of the amount of higher-priority jobs’ execution.
  This framework can be applied to other scheduling algorithms
    e.g., EDF, LLF, and potentially more
    Need to calculate the amount of higher-priority jobs’ execution.

## Slide 92: Global scheduling: response time analysis
Some finding of RM’s critical instant
  At most m-1 higher-priority carry-in jobs [GSY09]
    Carry-in job in an interval: released before the interval and having remaining execution at the beginning of the interval
  What happens if there are more than m-1 carry-in jobs?
    We can shift the interval of interest, which can increase the response time.
  How to incorporate this finding to RTA framework?
[GSY09] N. Guan, M. Stigge, W. Yi, G. Yu, New response time bounds for fixed priority multiprocessor scheduling, in: Proceedings of IEEE Real-Time Systems Symposium, 2009, pp. 387-397.

## Slide 93: Global scheduling: response time analysis
  How to incorporate this finding to RTA framework?
    The amount of execution of Task j in an interval of length L
      Ceil(L/Tj)*Cj
      Ceil((L+Tj-Cj) /Tj)*Cj
Cj
Cj
L
Cj
Cj
L
Cj
an+1 = Ci+Floor(∑Ceil((an+Tj-Cj)/Tj)*Cj/m)
Non-carry-in job
Carry-in job
Summation of Ceil(an/Tj)*Cj for all tasks +
Summation of Ceil((an+Tj-Cj)/Tj)*Cj - Ceil(an/Tj)*Cj for (m-1) largest task j

## Slide 94: Summary: Di = Ti
TFP
  RM-US: U ≤ 0.33*m
  RM: response-time analysis
    Some conditions for the critical instant
JFP
  EDF-US: U ≤ 0.5*m
  EDF: response-time analysis
JDP
  Fluid scheduling (optimal)
    U ≤ m (the only exact analysis in multiprocessor scheduling)

## Slide 95: Extension: Di = Ti → Di ≤ Ti
TFP
  RM-US: ∑ Ci/Di ≤ 0.33*m
  RM: response-time analysis
JFP
  EDF-US: ∑ Ci/Di ≤ 0.5*m
  EDF: response-time analysis
JDP
  Fluid scheduling (not optimal any more)
    ∑ Ci/Di ≤ m (not exact any more)
  Schedulability analysis for EDZL, FPZL and LLF

## Slide 96: Schedulability analysis driven optimal scheduling
TFP
  Why RM (DM)?
JFP
  Why EDF?

## Slide 97: TFP for multicore: beyond RM
A schedulability analysis exists for any arbitrary task-priority assignment for TFP.
Answer how to find optimal task-level priority
[DaBu11] R. I. Davis and A.Burn, Improved Priority Assignment for Global Fixed Priority Preemptive Scheduling in Multiprocessor Real-Time Systems, Real-Time Systems, 2011, pp. 1-40.

## Slide 98: TFP for multicore: beyond RM
Task-level optimal priority assignment
  Select iteratively a task for the lowest possible priority
A
B
C
D
E
Lowest Priority
Lowest Priority
Highest Priority
F

## Slide 99: JFP for multicore: beyond EDF
A schedulability analysis does not exist for any arbitrary job-priority assignment for JFP.
How to assign job-priority?
  Pseudo-deadlines: SPDF (Smallest Pseudo Deadline First)
Develop a schedulability analysis for any given job-priority assignment
Answer how to find optimal pseudo deadlines (job-level priority)
[CBC12] H. S. Chwa, H. Back, S. Chen, J. Lee, A. Easwaran, I. Shin, and I. Lee, Extending Task-level to Job-level Fixed Priority Assignment and Schedulability Analysis Using Pseudo-Deadlines, IEEE Real-Time Systems Symposium (RTSS), 2012, pp 51-62.

## Slide 100: JFP for multicore: beyond EDF
Job-level optimal priority assignment
  Optimal pseudo-deadline assignment
A
B
C
D
E
F
A
B
C
D
E
F

## Slide 101: More general task model
DAG or fork-join task model
Mixed-criticality task model

## Slide 102: Task model for parallel programming
DAG or fork-join task model
  For OpenMP, MapReduce
More room for improvement
[CLP13] H. S. Chwa, J. Lee, K. Phan, A. Easwaran, and I. Shin, Global EDF Schedulability Analysis for Synchronous Parallel Tasks on Multicore Platforms, Euromicro Conference on Real-Time Systems (ECRTS), 2013, pp 25-34.

## Slide 103: Mixed-criticality task model
Tasks have different criticality.
Priority according to criticality yields low utilization.
Can we improve utilization without compromising time constraints of both low- and high-criticality tasks?
  Exploit varying degrees of execution time assurance!
[LPG14] J. Lee, K. Phan, X. Gu, J. Lee, A. Easwaran, I. Shin, and I. Lee, MC-Fluid: Fluid Model-Based Mixed-Criticality Scheduling on Multiprocessors, IEEE Real-Time Systems (RTSS), 2014, pp. 41-52

## Slide 104: Scheduling theory towards practice
Practice
Theory
Soft deadline
Dependent task model, e.g., resource sharing
Hierarchical model (virtualization)
  m identical cores
  Hard deadline
  Independent periodic tasks
  Di = Ti
  Preemptable without any limit and overhead for context switch
Preemption cost
analysis
VxWorks, Xen, RT Linux
Di ≤ Ti
Non-preemptive scheduling

## Slide 105: Scheduling theory towards practice
A lot of movement towards practice
For example,
  [CBH14] Linux’s Processor Affinity API, Refined: Shifting Real-Time Tasks towards Higher Schedulability, RTSS 2014.
[CGB14] F. Cerqueira, A. Gujarati, B. B. Brandenburg, Linux’s Processor Affinity API, Refined: Shifting Real-Time Tasks towards Higher Schedulability, IEEE Real-Time Systems Symposium (RTSS), 2014, pp 249-259.

## Slide 106: Scheduling for Linux’s processor affinity
Task migration under current RTOSs
  Arbitrary Processor Affinities
Why processor affinities?
  Security: isolate tasks to prevent cache side-channel attacks
  Cache locality: avoid migration-related cache misses
  Energy efficiency: restrict non-critical tasks to small, power-efficient cores

## Slide 107: Scheduling for Linux’s processor affinity
Affinity (O) Priority (X)
τ1
τ2
τ4
P1
P2
P3
τ1
τ2
τ4
P1
P2
P3
τ3

## Slide 108: Scheduling for Linux’s processor affinity
Affinity (O) Priority (O)
τ1
τ2
τ4
P1
P2
P3
τ3
τ1
τ2
τ4
P1
P2
P3
τ3

## Slide 109: Scheduling for Linux’s processor affinity
Scheduling algorithm
  How to find the best matching?
Schedulability analysis
  How to incorporate the new matching into a schedulability analysis?

## Slide 110: Notice
궁금한 것이 있으시면 중간에 질문 부탁드립니다.
  쉬는 시간이나 Q&A 시간에 하셔도 좋습니다.
현업의 어플리케이션에 필요한 관련 내용 (작업 모델, 시스템)을 말씀해 주시면 답변을 드리거나 반영가능한 내용은 내일 강의 내용에 반영하겠습니다.

## Slide 111: Real-Time Scheduling
아래 예제로 돌아와서, 무슨 algorithm을 쓰고, 어떤 조건을 만족하면 모든 (영원히) schedulable 한가?
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
τ1
τ2
τ3
Deadline miss
τ1 > τ2 > τ3, non-preemptive
τ1 > τ2 > τ3, preemptive

## Slide 112: Real-Time Scheduling
왜 schedulability analysis가 필요한가? Simulation 해 보면 schedulability를 알 수 있지 않나?
  Offset이 바뀌어도 schedulable 한가? 모든 offset에 대해서 simulation?
  Execution이 max 보다 작게 되어도 여전히 schedulable 한가?
  주기의 최소 공배수가 매우 크면 simulation은 어떻게?
  …
Scheduling
Algorithm
Schedulability Analysis
Can we guarantee no deadline miss in the future?

## Slide 113: Real-Time Scheduling
무슨 scheduling algorithm을 쓰고, 어떤 조건을 만족하면 (즉, schedulability analysis) 모든 job이 영원히 deadline miss를 하지 않는가?
  Offset 에 관계없이?
  모든 실제 실행시간 ≤ WCET에 대해?
  주기의 최소 공배수가 매우 커도 보장이 가능?
Scheduling
Algorithm
Schedulability Analysis
예시
Can we guarantee no deadline miss in the future?

## Slide 114: Case Study
BMS system
  Task model
    초기화 작업을 제외하고는 periodic tasks
    Initialization task가 존재하나 start-up, shutdown 시에만 수행
  실행시간
    max execution time을 측정
  Task dependency
    Control flow dependency 없음
    Shared resource 경쟁 없음

## Slide 115: Case Study
왜 analysis가 필요한가?
  Q: (T,C)에서 최대 실행 시간대로 시간에 맞게 simulation 하면 schedulability를 알 수 있지 않는가?
  A: task model에 따라 scheduling anomaly 때문에 schedulability를 guarantee 할 수 없다
Execution이 더 짧아지는게 deadline miss를 일으키는 예제 설명