## Slide 1: Designing a Battery Management System From a Real-Time System Perspective
Jinkyu Lee
Dept. of Computer Science and Engineering,
Sungkyunkwan University (SKKU)
2022.9.21-22 Samsung SDI

## Slide 2: Instructor Information
Jinkyu Lee 이진규
  Associate Professor
    Department of Computer Science and Engineering 소프트웨어학과, SKKU (2014.3~)
  Postdoctoral Researcher
    Department of EECS, University of Michigan
      Advisor: Prof. Kang G. Shin
  B.S., M.S., Ph.D.
    Department of Computer Science 전산학부, KAIST
      Advisor: Prof. Insik Shin & Ikjun Yeom
Contact information
  Email. jinkyu.lee@skku.edu
  Website. https://rtclskku.github.io/website/jinkyulee.html
  Real-Time Computing Lab@SKKU. https://rtclskku.github.io/website

## Slide 3: Instructor Information
Research areas
  Real-time system
    ML (Machine learning) for RT, RT for ML
  Software-defined battery management
    Battery management systems
  Mobile system
Real-time system
Software-defined battery
management
Mobile
system
Specialty:
Real-time scheduling
- System design and analysis
with timing guarantees
- QoS support
- Resource management

## Slide 4: Instructor Information
Achievements: research
  IEEE RTSS (Real-Time Systems Symposium)
    Top 1 RT conference, about 30 papers published per year
    19 papers published
  IEEE RTAS (Real-Time and Embedded Technology and Application Symposium)
    Top 2 RT conference, about 30 papers published per year
    6 papers published
  SCI(E) Journals
    52 papers, including 17 IEEE/ACM transactions/journals
Achievements: professional activities
  TPC (Technical Program Committee): IEEE RTSS 2018, 2020, 2021 and 2022
  TPC: IEEE RTAS 2020, 2022 and 2023
  TPC co-chair: IEEE RTCSA 2020

## Slide 5: Instructor Information
Research example
  How to provide timing guarantees for software-defined networks?
MC-SDN: Supporting Mixed-Criticality Real-Time Communication Using Software-Defined Networking IEEE RTSS 2018

## Slide 6: Instructor Information
Research example
  How to minimize battery aging while providing timing guarantees of real-time tasks?
Battery Aging Deceleration for Power-Consuming Real-Time Systems
IEEE RTSS 2019

## Slide 7: Instructor Information
Research example
  How to fully utilize CPU and GPU for time-predictable execution for DNN tasks?
LaLaRAND: Flexible Layer-by-Layer CPU/GPU Scheduling for Real-Time DNN Tasks
IEEE RTSS 2021

## Slide 8: Overall Schedule
1차시 (신동화 교수님)
  9/19(월) 13~16시
  실시간 시스템의 개념
2차시
  9/21(수) 9~12시
  실시간 태스크 스케줄링 기법
3차시
  9/22(목) 13~16시
  실시간 태스크 스케줄링 가능성 (Schedulability) 분석 기법
추후
  배터리 관리 시스템의 태스크 구성과 스펙에 따른 실시간 시스템 성능 요구 분석 (현재 BMS 스펙 등을 검토 및 토의)
Designing a Battery Management System From a Real-Time System Perspective

## Slide 9: Schedule for each day
(9/21)
09:00 – 10:15
  Lecture
10:15 – 10:30
  Break
10:30 – 11:45
  Lecture
11:45 –
  Q&A
(9/22)
13:00 – 14:15
  Lecture
14:15 – 14:30
  Break
14:30 – 15:45
  Lecture
15:45 –
  Q&A

## Slide 10: RT SYSTEMS & RT SCHEDULING

## Slide 11: Real-Time System
Systems that operate with time constraints (deadlines)
  Important to produce accurate results before deadlines
  Usually for safety-critical systems or mission-critical systems
Automotive
Robots
Avionics
Multimedia
Factory Automation
Smartphones
Medical Devices
Military

## Slide 12: Real-Time System
Systems that operate with time constraints (deadlines)
  Important to produce accurate results before deadlines
  Usually for safety-critical systems or mission-critical systems
From Honda

## Slide 13: Real-Time System
Systems that operate with time constraints (deadlines)
  Important to produce accurate results before deadlines
  Usually for safety-critical systems or mission-critical systems
Chart: response time (avg=25, max=100)
Response Time | 10 | 21 | 23 | 14 | 23 | 19 | 23 | 42 | 12 | 32 | 100 | 12 | 12 | 19 | 21 | 23 | 43 | 28 | 23 | 27 | 18 | 23 | 25 | 19
Response Time | 10 | 21 | 23 | 14 | 23 | 19 | 23 | 42 | 12 | 32 | 100 | 12 | 12 | 19 | 21 | 23 | 43 | 28 | 23 | 27 | 18 | 23 | 25 | 19
Chart: response time (avg=50, max=60)
Response Time | 33 | 52 | 60 | 40 | 55 | 42 | 60 | 34 | 58 | 45 | 60 | 48 | 55 | 40 | 52 | 60 | 56 | 43 | 58 | 39 | 56 | 51 | 43 | 60
Response Time | 33 | 52 | 60 | 40 | 55 | 42 | 60 | 34 | 58 | 45 | 60 | 48 | 55 | 40 | 52 | 60 | 56 | 43 | 58 | 39 | 56 | 51 | 43 | 60

## Slide 14: Real-Time Systems: Research Topics
Cyber Physical Systems: Design Challenges, IEEE ISORC, 2008.
Applications
Languages
Operating Systems
Middleware
Architecture
Hardware
…
MC-SDN: Supporting Mixed-Criticality Real-Time Communication
Using Software-Defined Networking, IEEE IoT Journal, 2019.
Design time-predictable
computing systems
Timing guarantee and analysis
of computing systems
+

## Slide 15: Real-Time Scheduling
Platform
Task model
Constraints
Schedule all real-time tasks
such that there is no single job deadline miss
Some contents are from “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo.

## Slide 16: Real-Time Scheduling
Task models
  Single job
  Aperiodic
  Sporadic
  Periodic
  DAG-structured
  Gang-structured
  …
Constraints
  Precedence
  Shared resources
  Self-suspensions
  Mode changes
  Fully preemptive
  Fully non-preemptive
  Limited preemptive
  …
Platforms
  Uniprocessor
    …
  Multiprocessor
    …
  GPU + CPU
  Distributed
  …

## Slide 17: Real-Time Scheduling
Source: http://aar.faculty.asu.edu/research/mosart/mosart.html
sensor
control law
computation
A/D
reference input
D/A
T1
D1=4
T1=5
T1
τ1
= Task 1
D1
D1
C1=2
actuator
Job 1
Job 2
Job 3

## Slide 18: Real-Time Scheduling
Uniprocessor
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
τ1
τ2
τ3
T1=4, D1=4, C1=1

## Slide 19: Real-Time Scheduling
Uniprocessor
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
τ1
τ2
τ3
T1=4, D1=4, C1=1
Schedule all real-time tasks
such that there is no single job deadline miss
: at each time slot, only one job can be executed.
= Schedulable

## Slide 20: Real-Time Scheduling
Uniprocessor: at each time slot, only one job can be executed.
(4,1)
(5,2)
(7,2)
5
5
10
10
15
15
τ1
τ2
τ3
T1=4, D1=4, C1=1
Deadline miss
τ1 > τ2 > τ3, non-preemptive
τ1 > τ2 > τ3, preemptive

## Slide 21: Real-Time Scheduling
Task models
  Single job
  Aperiodic
  Sporadic
  Periodic
  DAG-structured
  Gang-structured
  …
Constraints
  Precedence
  Shared resources
  Self-suspensions
  Mode changes
  Fully preemptive
  Fully non-preemptive
  Limited preemptive
  …
Platforms
  Uniprocessor
    …
  Multiprocessor
    …
  GPU + CPU
  Distributed
  …

## Slide 22: Real-Time Scheduling
Optimization criteria
  Feasibility
  Response time
  Maximum lateness
  Utilization bandwidth
  Energy consumption
  Temperature
  Number of processors
Schedule all real-time tasks
such that there is no single job deadline miss

## Slide 23: Real-Time Scheduling
Industrial/practical usage of real-time scheduling
  Rate Monotonic is used in most industrial settings.
  Priority Inheritance is in most RT kernels.
  Sporadic Server is specified in POSIX.
  CBS is implemented in LINUX.
  EDF is now supported by a few kernels
    Erika Enterprise: certified OSEK and adopted by Magneti Marelli in next generation ECUs
    Ada 2005 runtime support
    Linux: SCHED_DEADLINE in mainline since June 2014
  A lot of RT Tools are now available for
    WCET estimation, schedulability analysis, scheduling simulation, formal verification, etc.

## Slide 24: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 25: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 26: Real-Time Scheduling
A practical example of real-time scheduling
  What is the physical meaning of 1/4 + 2/5 + 2/7?
    Utilization
    What if the utilization is larger than 1.0?
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 27: Real-Time Scheduling
A practical example of real-time scheduling
  Example: 1/4 + 2/5 + 2/7 <= 0.7
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 28: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 29: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 30: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 31: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo

## Slide 32: Real-Time Scheduling
A practical example of real-time scheduling
From “Real-Time Systems: Achievements and Perspectives” by Giorgio Buttazzo
Why this is possible?
Scheduling algorithm + Schedulability analysis

## Slide 33: Real-Time Scheduling
Task model, constraints and platform are usually given.
Then, how can we achieve timeliness of a real-time systems?
Schedule all real-time tasks
such that there is no single job deadline miss

## Slide 34: Real-Time Scheduling
From now on, we focus on the following periodic/sporadic task model
  τi :Task i
    Ti: the minimum separation / period
    Ci: the worst-case execution time (WCET)
    Di: the relative deadline
  Job: an instance of a task
T1
D1=4
T1=5
T1
τ1 (5,2,3)
D1
D1
C1=2
Job 1
Job 2
Job 3
(7,2)
τ3
    (Ti, Ci , Di)
      Or
    (Ti, Ci), implying Ti = Di
Job 1
Job 2
τ1(T1,C1,D1)
τ3(T3,C3)

## Slide 35: Real-Time Scheduling
From now on, we focus on the following periodic/sporadic task model
  τi :Task i
    Ti: the minimum separation / period
    Ci: the worst-case execution time (WCET)
    Di: the relative deadline
  Where do these parameters come from?
    Ti and Di: usually from the target system (recall the hitting-obstacle example)
    Ci: empirically measured, or code analysis
      WCET analysis, under given platform

## Slide 36: Real-Time Scheduling
From now on, we focus on the fully preemptive constraint and a uniprocessor platform.
  A higher-priority job can preempt a currently-executing lower-priority job.
  At each time slot, only one job can be executed.
Where do these constraints/platforms come from?
  Usually from the target system and its design

## Slide 37: Real-Time Scheduling
Scheduling goal
  Under the periodic/sporadic task model, the fully preemptive constraint, and a uniprocessor platform
Two main components for real-time scheduling
  Scheduling algorithm
    Determine when each job executes (which job to be executed)
  Schedulability analysis
    Guarantee no deadline miss of a given task set under the target scheduling algorithm
Schedule all real-time tasks
such that there is no single job deadline miss
Exact (sufficient and necessary)
Only sufficient

## Slide 38: Real-Time Scheduling
Two main components for real-time scheduling
  Scheduling algorithm
    Determine when each job executes (which job to be executed)
  Schedulability analysis
    Guarantee no deadline miss of a given task set under the target scheduling algorithm
Scheduling
Algorithm
Can we guarantee no deadline miss in the future?
Schedulability Analysis

## Slide 39: Real-Time Scheduling
Why do we need schedulability analysis? Isn’t it possible to guarantee schedulability simply by simulating a target set of tasks?
  Is it possible to simulate all different combinations of offsets?
  Can each simulation guarantee the schedulability even with actual execution times less than their corresponding WCETs?
  Is it feasible to simulate a target set of tasks if their LCM is very large?
Scheduling
Algorithm
Schedulability Analysis
Can we guarantee no deadline miss in the future?

## Slide 40: Real-Time Scheduling
Which scheduling algorithm with which condition (i.e., schedulability analysis) guarantees that there is no single job deadline miss forever?
  With any offset,
  With any actual execution time,
  With any arbitrary long period,
Scheduling
Algorithm
Schedulability Analysis
Example
Can we guarantee no deadline miss in the future?

## Slide 41: UNIPROCESSOR SCHEDULING

## Slide 42: Real-Time Scheduling
Let’s focus on the most popular (simplest) setting.
  A single processor
  Hard deadline
  Independent periodic tasks
  Relative deadline = period (Di = Ti)
  Preemptable without any limit
  No overhead for context switch

## Slide 43: Real-Time Scheduling
How can this setting be extended?
Practice
Theory
Soft deadline
Dependent task model, e.g., resource sharing
Hierarchical model (virtualization)
  A single processor
  Hard deadline
  Independent periodic tasks
  Di = Ti
  Preemptable without any limit and overhead for context switch
Preemption cost
analysis
VxWorks, Xen, RT Linux
Di ≤ Ti
Non-preemptive scheduling

## Slide 44: Clock-Driven Task Scheduling
Clock-driven
  a schedule determines (off-line) which job to be executed at each instant
  static or cyclic
  predictable and deterministic
  scheduler: invoked by a timer
  multiple tables for different operation modes
T1= 6, C1= 3, D1= 6
T2= 8, C2= 3, D2= 8 Major cycle = lcm (6,8) = 24

## Slide 45: Pros and Cons of Cyclic Schedule
Pros
  Simple, table-driven, easy to validate (knows what’s going on at any moment)
  Fits well for harmonic periods and small system variations
  Static schedule => deterministic, static resource allocation, no preemption
  Small jitter
Cons
  Difficult to change (need to re-schedule all tasks)
  Fixed released times for the set of tasks
  Difficult to deal with different temporal dependencies
  Scheduling algorithm may become complex (NP-hard)
  Doesn’t support aperiodic and sporadic tasks efficiently

## Slide 46: Round-Robin Task Scheduling
Weighted Round-robin
  Interleave job executions
  Allocate a time slice to each job in the FIFO queue
  Time slice may vary while sharing the processor
  Good for pipelined jobs, e.g., network packets
T1= 6, C1= 3, D1= 6
T2= 8, C2= 3, D2= 8 Major cycle = lcm (6,8) = 24

## Slide 47: Priority-Driven Task Scheduling
Priority-driven
  The highest-priority job gets to run until completion or blocked
  A processor is never idle if ready jobs are waiting (work-conserving)
  Preemptive or non-preemptive
  Priority assignment can be static or dynamic
  Scheduler just looks at the priority queue for waiting jobs (list schedule)
T1= 6, C1= 3, D1= 6
T2= 8, C2= 3, D2= 8 Major cycle = lcm (6,8) = 24

## Slide 48: Priority-Driven Task Scheduling
Why priority-driven scheduling algorithm?
  Use priority to represent urgency/importance
  Easy implementation of scheduler (compare task priorities and then dispatch tasks accordingly)
  Tasks can be added or removed easily
  No direct control of execution instant

## Slide 49: Classification of Priority-Driven Scheduling
Task-level fixed-priority (TFP): all jobs of a periodic task have the same fixed priority
    RM (Rate-monotonic) [Liu and Layland 1973] – the higher the task frequency, the higher its priority
Task-level dynamic-priority: different priorities to individual jobs of a periodic task
  Job-level fixed-priority (JFP): priority of each job is fixed
    EDF (Earliest Deadline First) [Liu and Layland 1973]
  Job-level dynamic-priority (JDP): priority of each job can change over time
    LLF (Least Laxity First) [Leung 1989]
Less Overhead
More
Expressive
TFP
JFP
JDP
< Expressiveness> >

## Slide 50: Classification of Priority-Driven Scheduling
Task-level fixed-priority (TFP): all jobs of a periodic task have the same fixed priority
    RM (Rate-monotonic) [Liu and Layland 1973] – the higher the task frequency, the higher its priority
Task2
T2=5
C2=3
Task1
T1=3
C1=1
(3,1)
τ1
(5,3)
τ2

## Slide 51: Classification of Priority-Driven Scheduling
Job-level fixed-priority (JFP): priority of each job is fixed
  EDF (Earliest Deadline First) [Liu and Layland 1973]
Task2
T2=5
C2=3
Task1
T1=3
C1=1
(3,1)
τ1
(5,3)
τ2

## Slide 52: Classification of Priority-Driven Scheduling
Job-level dynamic-priority (JDP): priority of each job can change over time
  LLF (Least Laxity First) [Leung 1989]
2
2
1
2
2
1
1
2
2
2
Task2
T2=5
C2=3
Task1
T1=3
C1=1
(3,1)
τ1
(5,3)
τ2

## Slide 53: Classification of Priority-Driven Scheduling
Can we guarantee no deadline miss of all jobs of a given task set under each scheduling algorithm?
  TFP: RM
  JFP: EDF
  JDP: LLF
What is the maximum utilization?
  U = ∑ Ci/Ti ≤ 1.0
    Example: 1/4 + 2/5 + 2/7
Can each scheduling algorithm achieve the maximum utilization?

## Slide 54: RM: Overview
  Critical instant under RM
Utilization-based analysis
  U ≤ n(21/n – 1.0)
    n → ∞, n(21/n – 1.0) → 0.69
  Only sufficient
Response-time analysis
  Exact
Some applications
  Schedulability with transient overhead, interrupts and blocking
Without loss of generality
T1 ≤ T2 ≤… ≤ Tn

## Slide 55: RM: Critical Instant
Critical instant of τi
  A job of τi arriving at that instant has the largest response time
  Which τ2 has the maximum response time?
In-phase instant is critical under RM
  All higher priority tasks are released at the same instant of Ji,c (assume all jobs are completed before the next job is released)
Task1 Task2
Task1, Task2
Task2 Task1
Why?

## Slide 56: RM: Utilization-Based Analysis
Let’s consider two tasks
  Task2 can only be executed when Task1 is not in the system.
Let T2 < 2T1. Determine the maximum schedulable C2.
  If T2 ≤ T1+C1, max(C2) = T1 – C1
    U=C1/T1+ (T1-C1)/T2
  Else, max(C2)=T2-2C1
    U=C1/T1 + (T2-2C1)/T2
e1
e1
e1
0 p1 2p1
p2
p2
maximal e2
  Proof of U ≤ n(21/n – 1.0)

## Slide 57: RM: Utilization-Based Analysis
Given C1, T1, and T2, plot U
The minimum U occurs when
  T2 = T1+C1
  where U = C1/T1+(T1-C1)/(T1+C1)
What is the minimum U?
  Take the derivative w.r.t T1 and set dU/dT1=0
  We will get C1=(21/2-1.0)T1 and U=0.828
General cases with n
T2=T1 T2=nT1
U
1
  RM-schedulable if U ≤ n(21/n – 1.0)

## Slide 58: RM: Utilization-Based Analysis
Example
  Total utilization is
.200 + .267 + .286 = .753 < U(3)=3(21/3 – 1.0)=.779
  The periodic tasks in the example are schedulable according to the UB test.
 | Ci | Ti | Ui
Task1 | 20 | 100 | 0.200
Task2 | 40 | 150 | 0.267
Task3 | 100 | 350 | 0.286

## Slide 59: RM: Utilization-Based Analysis
Example
  Total utilization is
  .400 + .267 + .286 = .953 > U(3)=3(21/3 – 1.0) =.779
  UB test cannot deem the task schedulable.
    Try the exact analysis
 | Ci | Ti | Ui
Task1 | 40 | 100 | 0.400
Task2 | 40 | 150 | 0.267
Task3 | 100 | 350 | 0.286

## Slide 60: RM: Response-Time Analysis
Response time analysis
  The duration between a job’s release time and finishing time
  Test terminates when an+1 = an
  Task i is schedulable if its response time is before its deadline: an ≤ Ti
    an is the response time of Taski
  Can be applied to any TFP
    Not only RM, but also any TFP
Without loss of generality
T1 ≤ T2 ≤… ≤ Tn
A set of higher-priority tasks

## Slide 61: RM: Response-Time Analysis
Without loss of generality
T1 ≤ T2 ≤… ≤ Tn
A set of higher-priority tasks

## Slide 62: RM: Response-Time Analysis
  How does this work? --- Task3 is schedulable?
 | Ci | Ti | Ui
Task1 | 40 | 100 | 0.400
Task2 | 40 | 150 | 0.267
Task3 | 100 | 350 | 0.286

## Slide 63: RM: Response-Time Analysis
a3 = a2 = 300 Done!
Task is schedulable using RT test.
  a3 = 300 < T3 = 350

## Slide 64: RM: Response-Time Analysis
Why does this work?
  Time-demand analysis based on critical instant
  If Ji is done at t, then the total work must be done in [0,t] is (from Ji and all higher priority tasks): time demand function
  Can we find t ≤ Di such that wi(t) ≤ t
    Cannot check all t [0, di]
    Check all arrival instants and di
t
w(t)
time
Di

## Slide 65: RM: Transient Overload
Question: what if the task with a smaller period is not important to the underlying application?
Answer: consider period transformation, period aggregation or period splitting
Example: consider the following unschedulable task set
τi | Ci | ECi (avg exec time) | Ti | comments
τ1 | 20 | 10 | 100 | 
τ2 | 30 | 25 | 150 | 
τ3 | 80 | 40 | 210 | Non-critical
τ4 | 100 | 20 | 400 | 

## Slide 66: RM: Transient Overload
Solution 1: reduce Task3’s priority by lengthening its period, possible only if Task3's relative deadline can be greater than its original period. In such a case, replace Task3 by two tasks Task30 and Task300, each with period 420, WC exec times C30 = C300 = 80, avg exec times a30 =a300 =40. Task30 and Task300 must be phased to be 210 time units apart. If the set {Task1, Task2, Task30, Task300, Task4} is RM-schedulable, done.

## Slide 67: RM: Transient overload
Solution 2: increase Task4’s priority by splitting each invocation into two: Task40: C40 = C4/2, a40 = a4/2, T40 = T4/2
  {Task1, Task2, Task4} or {Task1, Task2, Task40} are schedulable

## Slide 68: EDF: Schedulability Analysis
RM’s critical instants hold for EDF??
  Why or why not?

## Slide 69: EDF: Schedulability Analysis
EDF is schedulable iff U ≤ 1.0
  U = 1/4 + 2/5 + 2/7
How to prove?
  Using busy interval

## Slide 70: EDF: Schedulability Analysis
Example
  A digital robot with EDF schedule
    Control loop: Cc≤ 8ms at 100Hz
    BIST (Built-in-Self-Testing): Cb≤ 50ms
    BIST can be done every 250ms
  Add a telemetry task to send and receive messages with Ct≤ 15ms
    If BIST is done every 1000ms
    The telemetry task can have a relative deadline of 100ms
      Sending or receiving must be separated by at least 100ms

## Slide 71: Summary: Di = Ti
TFP: RM
  U ≤ n(21/n – 1.0)
  Response-time analysis (exact)
JFP: EDF
  U ≤ 1 (exact)
JDP: LLF
  U ≤ 1 (exact)
The three algorithms are optimal for each category.
All the results hold for sporadic tasks.

## Slide 72: Extension: Di = Ti → Di ≤ Ti
TFP: DM (deadline monotonic)
  ∑ Ci/Di ≤ n(21/n – 1.0)
  Response-time analysis: an ≤ Di, still exact
JFP: EDF
  ∑ Ci/Di ≤ 1
    Not exact, but there exists another exact analysis.
JDP: LLF
  ∑ Ci/Di ≤ 1
The three algorithms are still optimal for each category.
All the results hold for sporadic tasks.

## Slide 73: Extension: Di = Ti → Di ≤ Ti
JFP: EDF
  Any exact analysis?

## Slide 74: Extension: Di = Ti → Di ≤ Ti
JFP: EDF
  Any exact analysis?
    ∑ DBF(Taski, t) ≤ t, for all t>0
  Proof
    Busy interval

## Slide 75: Where are we?
Practice
Theory
Soft deadline
Dependent task model, e.g., resource sharing
Hierarchical model (virtualization)
  A single processor
  Hard deadline
  Independent periodic tasks
  di = pi
  Preemptable without any limit and overhead for context switch
Preemption cost
analysis
VxWorks, Xen, RT Linux
Di ≤ Ti
Non-preemptive scheduling

## Slide 76: How to Apply to This a Target System?
Check
  Task model
    Any dependency?
    Any shared resources?
    (T, C, D) is given?
  Platform
  Constraints

## Slide 77: SYNCHORNIZATION

## Slide 78: CASE STUDY: BMS SYSTEM